Boxlight Corporation

Installation Procedures for the Navatar lens in the PRO4500DP

Thank you for purchasing your new lens from Boxlight.

The procedure is as follows:

- Loosen the screw on the rear of the unit and remove the lamp cover. This is done by sliding it back about ½ inch and then lift up.

- CAUTION:   The top case is attached with two wire connectors to the main board. Be careful not to pull the top case off to hard

- Behind the lamps, toward the rear of the projector, you should see 2 black screw heads. Remove these screws and the top case should be ready to come off.

- Remove the top case by lifting/pulling the rear near the lamps up. You will have about 2-3 inches when the rear is lifted.

- Look forward of the lamps on the left side and you should see you two wire plugs going to the board. Removed these plugs by pulling straight up.

- Once the wires are free, the rest of the case should be free to lift up and move forward to remove.

- Unplug the wire going to the lens assy.

- Remove the large bezel from around the lens assy.

- Using a very small Phillips screwdriver, remove the small screw holding on the bezel to the lens. There should be a small hole to access the screw on the top of the bezel.

- Remove the 3 Philips screws around the base of the lens assy. There are two on the top and one on the bottom.

- Carefully remove the lens.

Lens reinstallation

Procedure follows:

- Install the Navatar lens with the supplied Philips screws. (Remove the lens caps from both ends on the new lens)

- If there is a wire plug with the new lens, please attach to the wire plug on the projector.

- Reinstall the larger bezel into the slots in the front of the case. The smaller bezel will not be used and the opening left in the front of the projector is required for lens adjustment. ( Note: depending on the lens to be installed, the larger bezel may not be used)

- Replace the top cover by placing the front of the case to the front of the projector. There is a tab on each front corner that will fit into slots in the projector.

- The case should now be able to be lowered.

- Make sure the wires from the top case are reattached. The plugs are different sizes so they will only fit into the proper place.

- Finish lowering the case and reinstall the 2 screws into the rear of the case.

- Reinstall the lamp door.